## Slide 1: Lincoln Laboratory Ad-hoc MIMO Adaptive Communication Simulation Tool
Adam Margetts, Derek Young, Bruce McGuffin, Dan Bliss, Glenn Fawcett, and Lloyd the Llama
DISTRIBUTION STATEMENT A. Approved for public release. Distribution is unlimited.
This material is based upon work supported by the Defense Advanced Research Projects Agency under Air Force Contract No. FA8702-15-D-0001. Any opinions,findings, conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the Defense Advanced Research Projects Agency. © 2019 Massachusetts Institute of Technology

## Slide 2
DISTRIBUTION STATEMENT A. Approved for public release.
Distribution is unlimited.
This material is based upon work supported by the Defense Advanced Research
Projects Agency under Air Force Contract No. FA8702-15-D-0001. Any opinions,
findings, conclusions or recommendations expressed in this material are those
of the author(s) and do not necessarily reflect the views of the Defense
Advanced Research Projects Agency.
© 2019 Massachusetts Institute of Technology.
Subject to FAR52.227-11 Patent Rights - Ownership by the contractor (May 2014)
The software/firmware is provided to you on an As-Is basis
Delivered to the U.S. Government with Unlimited Rights, as defined in DFARS
Part 252.227-7013 or 7014 (Feb 2014). Notwithstanding any copyright notice,
U.S. Government rights in this work are defined by DFARS 252.227-7013 or
DFARS 252.227-7014 as detailed above. Use of this work other than as
specifically authorized by the U.S. Government may violate any copyrights
that exist in this work.

## Slide 3: Simulation Environment Overview
MIMO Systems
Ad-hoc Networks
Multipath
Propagation Losses
CorrelatedShadowing
Interference
Cognitive
Comms
Space-Time-Frequency Correlation
Dynamic center frequencies
Notes: This is a representative scenario we would like to emulate

## Slide 4: Simulation Capabilities
Operate multiple radio nodes simultaneously and asynchronously
Generate realistic space-time-frequency MIMO fading channels
Model propagation over a variety of environments:
  Urban, suburban, rural
  Indoors, outdoors, fixed, mobile, or airborne
  Line-of-sight or non-line-of-sight
  Link lengths meters to tens of kilometers
  Frequencies: 10 MHz to 6 GHz

## Slide 5: Problem Set
Cognitive Radios
Ad-hoc Radio Networks
MIMO Communications
Motivating Scenarios:
LLAMAComm combines all three!

## Slide 6: Adaptive Cognitive Radio
Radio spectrum is underutilized
Cognitive radios identify and occupy time-frequency gaps
Requires simulating a wide range of center frequencies
Spectrum Occupancy
Time (Sec)
Frequency (MHz)
0
.25
-1.0
.5
0
1.0
1.5
Received Power (dBm)
.5
.75
1.0
-.5
-1.5
-140
-120
-100
-80
-60
-40
-20
Cognitive Radio Scenario

## Slide 7: Wireless Ad-hoc Networks
Formed dynamically
Multi-hop communications
Nodes interact asynchronously
Simulation provides datalink layer control
Ad-Hoc Network Scenario

## Slide 8
MIMO Communication Multiple-Input Multiple-Output
Arrays of antennas at transmitter and receiver
Increases reliability and throughput
Adaptively nulls interference sources
Simulate space-time-frequency correlations
MIMO Communications Example

## Slide 9: Available Wireless Network Simulators
Opnet
  Commercial
  Probabilistic physical layer
Ns2
  Open source (large research user base)
  Probabilistic physical layer
QualNet
  Commercial
  Probabilistic physical layer
ISIS Prowler (Probabilistic Wireless Network Simulator)
  Gyula Simon (Vanderbilt University)
  Written in Matlab
  Probabilistic physical layer
SWANS (Scalable Wireless Network Simulator) (built on JiST)
  Claimed 1,000,000 nodes simulated on a PC
  Probabilistic Physical Layer
Numerous cell-site planning tools
Wireless Insight (cousin to XFDTD)
  Solves Maxwell Equations
Physical Layer
Too Simple
Too Complex
Simulation should be as simple as possible, but no simpler

## Slide 10: LLAMAComm Overview
LLAMAComm is a MATLAB simulation tool
Simulates cognitive Multiple-Input Multiple-Output (MIMO) ad-hoc wireless networks
LLAMAComm
User-Defined Functions and Parameters
Results
Statistical Environment Models
Recorded Interference
Timing Support
Start
Decide
Done
Transmit
Receive

## Slide 11: LLAMAComm Timing Diagram Example
Complex datalink simulations are possible
  Colors indicate center frequency
Cognitive
Radios
Interference
Spectrum
Monitoring
Sync Tx
Pilot Tx
Pilot Rx
Sync Rx
Control Tx
Control Rx
Uplink Rx
Downlink Rx
Downlink Tx
Downlink Rx

## Slide 12: LLAMAComm Requirements
MATLAB R2009b or later
  Signal processing toolbox
Familiarity with MATLAB programming
Fast processor

## Slide 13: Scope of LLAMAComm Path Loss Models
Input parameter range
  frequency: 10 MHz – 6 GHz
  range: 1 m – 300 km(1)
  antenna height: 1 m – 10 km
Supported environments
  urban/suburban/rural
  in-building/building penetration/ outdoors
Model Outputs
  log-normal shadowing loss
    median power loss
    standard deviation
    shadowing correlation with angle
  multipath fading
    Rice k-factor
    delay spread
(1) Longer ranges only required for very high receivers
Urban
Rural
Median Path Loss (dB)
Median Path Loss (dB)

## Slide 14: Path Loss Example
Examine path loss from Interferer to Receiver
  Urban environment
  Outdoors
  Receiver below roof height
  Range > 1 km
Transmitter
Receiver
Interferer
Path Loss Example

## Slide 15: Path Loss Model 10 MHz-6 GHz, 10 m–20 km, Multiple Environments & Sites
Both outdoors
Terminal Sites:
Both indoors...
One indoors…
Environment:
Rural…
Urban
Suburban...
Below roof height,
Above roof height and below 200 m
Terminal Heights:
(Lower/Higher)
Below roof height, Below roof height…
Below roof height,
Near roof height…
Below roof height, Above
200 m…
Above roof height,
Below 1000 m…
Above roof height,
Above 1000 m…
Assumed LOS to NLOS Transition
Median Path Loss (dB) in Urban Environment, Avg. Building Height 18 m, Tx Height 2 m, Rx Height 30 m
Setting and Terminal Data:
Environment?
Indoors/Outdoors?
Indoor Range
External Wall Type
(concrete)
# Internal Walls
External Wall Angle
Terminal Heights?
Avg. Building Height
Range?
Center Frequency?
Range < 50 m…
Range < 1 km…
Range > 1 km
(max depends on freq)
Range:
Frequency:
Path Loss Median/
Standard deviation,
(Model Also Provides
Rice K-Factor,
Shadow-Loss Correlation Between Links)
Freq < 150 MHz (Longley-Rice w/Urban Correction/
Okumura-Sigma)
150 MHz < Freq < 1500 MHz
(Hata/Okumura-Sigma)
Freq > 1500 MHz
(Hata w/ COST Freq. Correction, Okumura-Sigma)
Existing Models,
Extensions or Modifications of Existing Models, or New Models As Required
Range (km)
Frequency (MHz)
Notes: Blue is path loss, pink is standard deviation

## Slide 16: Urban/Suburban Path Loss Models at 2 GHz Node 1 Indoors
a)
b)
c)
d)
Indoors
Indoors to LOS outdoors
Below roof height
Above roof height
In-room composite model
In-building (NLOS) composite model
Assumed max. range for LOS to building. Use NLOS building penetration model plus outdoor path loss model for greater ranges.
Assumed mean roof-height varies with environment
1 m
3 m
10 m
30 m
100 m
300 m
3 km
30 km
100 km
300 km
1 km
10 km
10 km
1 km
300 m
100 m
30 m
10 m
3 m
3 km
1 m
Ground Range
Node 2 Antenna Height
a
b
COST-231 Building Penetration Model to LOS Exterior Node
With Frequency Extensions
Hybrid Urban/Suburban Model Plus LOS Above 200 m Or Beyond 20 km
Okumura-Hata Model & Cost-231 Frequency Extension
COST-231 Walfisch-Ikegami Model
c
d
Walfisch with Okumura Correction
Path loss model includes indoor-to-outdoor links
  Loss depends on range, antenna heights, frequency, etc.

## Slide 17: Correlated Shadowing
Example: Average SIR = 20 dB
Shadowing Std. Dev. = 10 dB
Copy Threshold = 10 dB
Copy Prob. Varies from 76% to 94%
x (dB)
Signal
Interferer
Links to Common Node Have correlated Shadow Loss
DAz, f
Interference
Shadowing Loss in dB is N(,si)
Signal Shadowing Loss in dB is N(,ss)
Copy Threshold
Average SIR
Probability
SIR > x
Shadow loss correlation reduces
signal-to-Interferer power variation
Probability SIR > x for correlated links
High Correlation
Low Correlation

## Slide 18: Shadowing Correlation Coefficient
Link shadow loss is correlated
  Depends on angle separation
Limited data available
  Graziano measured at 900 MHz around Washington Beltway1
  Similar results by van Rees at 150 MHz, 450 MHz, 900 MHz in The Hague2
Approximate Graziano’s measurements with bilinear fit
  Lower MSE than proposed functions found in literature
  Min > 0 reflects homogeneous environment in different directions
  Max < 1 reflects uncorrelated shadowing at far end of links
Measured Correlation
Bilinear Fit
Graziano Beltway Data1
Victor Graziano, “Propagation Correlations at 900 MHz”, IEEE Trans. Veh. Tech., Nov. 1978
Jan van Rees, “Cochannel Measurements for Interference Limited Small-Cell Planning”, Archiv Elek. Ubertrag., 1988, pp 318-320
Sheraton
Hotel
Reston, VA
Winchester, VA
Baltimore, MD
Azimuth difference f

## Slide 19: Channel Processing Example
Interferer operates at nearby center frequency
Causes interference
Transmitter
Receiver
Interferer

## Slide 20: Signal Representation
Channel
Channel
Passband Model
90o
x
+
x
90o
x
x
LPF
+
x
90o
x
+
x
x
LPF
+
STF Channel
Baseband Equivalent Model Used by LLAMAComm
Transmitter
Interferer
Received
Signal
Signal
Interferer
Received
Signal
+
Noise
+
Noise
Transmitter
Receiver
Interferer
x
x
Pathloss
Pathloss
STF Channel
STF (Space-Time-Frequency Selective)

## Slide 21: Channel Model Options
‘STFCS’ (Space-time-frequency-correlated scattering)
  Preserves spatial correlation
‘WSSUS’
  Wide-sense stationary
  uncorrelated scattering
  Exponential power profile
Time
Frequency
Doppler
Lag
Delay Spread
Doppler Spread
2-D FFT
‘LOS_AWGN’
  Line-of-sight path loss in AWGN channel
  For debugging only
Correlated Time-Frequency Channel Samples
Delay-Doppler Channel Taps
Time-Varying Filters
Time-Invariant

## Slide 22: ‘STFCS’ channel model option
‘STFCS’ channel model was developed at Lincoln
  Correlates signals over space, time, and frequency
The STFCS channel tensor is four dimensional:
R×T×D×L
  R receive antennas
  T transmit antennas
  D Doppler taps
  L lag taps
Space-Time-
Frequency
Selective
MIMO Channel

## Slide 23: SISO Channel with Doppler and Multipath
n
j
e
0
w
n
j
e
1
w
n
j
D-1
e
w
T
r
a
n
s
m
i
t
S
a
m
p
l
e
s
R
e
c
e
i
v
e
S
a
m
p
l
e
s
Single channel input
Time-frequency processing
Single channel output

Time-
Frequency
Selective
SISO Channel


+
]
[
n
x
]
[
n
y
(1 x L)
(R receive antennas x N samples)
(T transmit antennas x N samples)
Scalar Filter
Doppler Shift
D Doppler Taps
Doppler
Lag
Delay Spread
Doppler Spread
]
[
n
x
]
[
n
y

## Slide 24: Spatially Correlated Static MIMO Channel
Spatially correlated static MIMO channel:
  G is an R×T i.i.d. Gaussian matrix
  U and V are random unitary matrices
   controls spatial correlation
What about MIMO channels with Doppler and Multipath?
  Create time-frequency-space correlations
H

## Slide 25: Sample the Time-Frequency Plane
t coherence time
f coherence bandwidth
Different Hi,j’s are uncorrelated with each other
Each Hi,j is spatially correlated
TLCB is longest coherent block (environment property)
Time
Frequency

## Slide 26: Interpolate the Time-Frequency Plane
Preserve spatial correlation
Time
Frequency

## Slide 27: Convert to Doppler-Lag Plane
Take 2-D FFT over each spatial component
  Time -> Doppler
  Frequency -> Lag
Doppler
Lag
Time
Frequency
Delay Spread
Doppler Spread
2-D FFT

## Slide 28: MIMO Channel with Doppler and Multipath
n
j
e
0
w
n
j
e
1
w
n
j
D-1
e
w
]
[
n
X
]
[
n
Y
T
r
a
n
s
m
i
t
S
a
m
p
l
e
s
R
e
c
e
i
v
e
S
a
m
p
l
e
s
Vector signal input
Space-time-frequency processing
Vector signal output
Space-Time-
Frequency
Selective
MIMO Channel
+
]
[
n
X
]
[
n
Y
(R x T x L)
(R receive antennas x N samples)
(T transmit antennas x N samples)
Matrix Filter
Doppler Shift
D Doppler Taps
Doppler
Lag
Delay Spread
Doppler Spread




## Slide 29: Building a Node Object in LLAMAComm
Example: building a receiver node
Note: A node can have any number of modules
name = ‘Receiver_module’;
callbackFcn = @receiver;
fc = 850e6;
type = ‘receiver’;
antPosition = [0 -1 2 …
Module Properties
name = ‘Receiver_node’;
location = [0 0 10];
velocity = [0 0 0];
controllerFcn = @Controller;
…
Node Properties
observedBlocks = 0;
nBlocksToObserve = 10;
blockLength = 5000;
…
User Parameters
RX
Receiver
Controller
RX
module
Class
Constructor
node
Class
Constructor
Node Object
Module Object
Set
User
Parameters

## Slide 30: Simulation Procedure
Controllers request to transmit and receive
Arbitrator enforces causality
Go to step 1.
Transmitter
Receiver
Interferer
Controller
TX
Transmitter
RX
Receiver
Controller
TX
Interferer
Environment
Controller
Arbitrator
Notes: Arbitrator enforces causality into the simulation

## Slide 31: Flowchart of the Arbitrator
Arbitrator Start
Request
Done
Call Transmit
Function
Store Transmit
Signal
Request
Done
Store Received
Signals
Call Receive
Function
Request
Done
Query
Modules
Combine
Received Signals
Arbitrator End
Complete?
Request?
No
No
Wait Request
Tx Request
Rx Request
Loop once per module
Arbitrator is the mailman

## Slide 32: Receiver Controller State Machine
start
receive_wait
done
If RX Done
Request RX
count ++
If RX Not Done
Do Nothing
Request RX
count = count + 1
If RX Done & count >= N
set module to Done
Text Color Key:
Red: Input from Arbitrator
Blue: Request
Black: Inline Code
Functionality:
Receive N sample blocks
Controller
TX
Transmitter
RX
Receiver
Controller
TX
Interferer
Environment
Controller
Arbitrator
1
3
2
4
Interferer
Transmitter
Receiver
Timing Diagram
sample time

## Slide 33: Receiver Controller Matlab Code
p = GetUserParams(nodeobj); % Load the user parameters
currState = GetNodeState(nodeobj); % Load the current state
switch currState
case 'start'
nodeobj = SetModuleRequest(nodeobj,'observer_rx','receive',p.blockLen);
p.observedBlocks = p.observedBlocks + 1;
nextState = 'receive_wait';
case 'receive_wait'
requests = CheckRequestFlags(nodeobj); % Get request flag
if requests==0 % if RX Done
if p.observedBlocks>=p.nBlocksToObserve;
nodeobj = SetModuleRequest(nodeobj,'observer_rx','done');
nextState = 'done';
else % Receive another block and increment counter
nodeobj …
= SetModuleRequest(nodeobj,'observer_rx','receive',p.blockLen);
p.observedBlocks = p.observedBlocks + 1;
nextState = 'receive_wait';
end
else % Wait until block has been received
nextState = 'receive_wait';
end
case 'done'
nextState = 'done'; % Continue in Done state
status = 'done';
end
nodeobj = SetNodeState(nodeobj,nextState); % Set the next state
nodeobj = SetUserParams(nodeobj,p) % Set the user parameters
Start
receive_wait
Done
If RX Done
Request RX
count ++
Request RX
count = count + 1
If RX Done & count >= N
set module to Done
If RX Not Done
Wait
Text Color Key:
Red: Input from Arbitrator
Blue: Request
Black: Inline Code

## Slide 34: Timing Diagram
LLAMAComm produces a timing diagram to simplify debugging
Each segment represents a transmit or receive sample block
Thin segments represent ‘wait’ blocks
Timing Diagram
Notes: Picture shows LLAMAComm scenario with 6 radios.
Signals processed in a block-wise fashion. Blocks are referred to as segments. 100-10K+ samples.
Block lengths can be different, but all blocks are processed at the same sample rate.
So, a particular receive segment requires that all transmit segments are processed first.
Numbers show the order the blocks were processed in. Goal of LLAMAComm is to make the order of simulation transparent.

## Slide 35: Timing Diagram Callback Plots
Clicking on a segment produces a plot
Plots can be customized by the user
Timing Diagram

## Slide 36: Node Position Map
LLAMAComm plots a map of node positions.
Clicking on a node name will produce a plot of the antenna positions and look directions.

## Slide 37: Future for LLAMAComm
Ground-to-Air link path loss model update
Nodes in Motion (long time scales)
  Time-varying path losses
Enhanced radio library
  Open source model?
Parallelism
  Parallel processing to reduce simulation time
Special interference modules that generate samples only when overlapping in frequency with a receive request
Allow dynamic sampling rates